## Slide 1: Electrical Circuits EEE-281 Lecture Notes
Dr. Özçel Cangül
Lecture Notes by Dr. Ali Muhtaroğlu
Fall 2023
METU Northern Cyprus Campus
References:
Electric Circuits 10th Ed. by Nilsson & Riedel
Electrical Circuit Analysis 3rd Ed. by Johnson, Johnson, Hilburn, and Scott
Engineering Circuit Analysis 7th Ed. by Hayt, Kemmerly, and Durbin
Fundamentals of Electric Circuits 3rd Ed. by Alexander, and Sadiku

## Slide 2: Introduction to Electrical Circuits Week 1 Reading: Nilsson & Riedel Chapter 1
Ali Muhtaroğlu

## Slide 3: What is an Electrical Circuit ?
A mathematical model for how physical circuits operate to transfer energy from one point to another
Ali Muhtaroğlu

## Slide 4: What is an Electrical Circuit ?
A mathematical model for how physical circuits operate to transfer energy from one point to another
Circuit theory can be used to analyze circuits instead of electromagnetic field theory if following assumptions can be made:
  Electric effects are instantaneous, which enables a lumped-parameter system model (resistors, capacitors, inductors, etc.)
    Signal wavelength, λ=c/f > 10 x physical dimensions of power system e.g. For 109 Hz radio signal,
    dimension < (3.108 m/s) / (109 cycles/s . 10) = 0.03 m
Ali Muhtaroğlu

## Slide 5: What is an Electrical Circuit ?
A mathematical model for how physical circuits operate to transfer energy from one point to another
Circuit theory can be used to analyze circuits instead of electromagnetic field theory if following assumptions can be made:
  Electric effects are instantaneous, which enables a lumped-parameter system model (resistors, capacitors, inductors, etc.)
    Signal wavelength, λ=c/f > 10 x physical dimensions of power system e.g. For 109 Hz radio signal,
    dimension < (3.108 m/s) / (109 cycles/s . 10) = 3 cm
  Net charge on every component in the system is zero
  No magnetic coupling between any pair of system components
Ali Muhtaroğlu

## Slide 6: Basic Electrical Engineering Design Flow
DESIGN SPECIFICATION
Ali Muhtaroğlu
CIRCUIT ANALYSIS / ENGINEERING
(what this course is about)

## Slide 7: Basic Electrical Engineering Design Flow
Concept
DESIGN SPECIFICATION
Ali Muhtaroğlu
CIRCUIT ANALYSIS / ENGINEERING
(what this course is about)

## Slide 8: Basic Electrical Engineering Design Flow
DESIGN SPECIFICATION
Ali Muhtaroğlu
CIRCUIT ANALYSIS / ENGINEERING
(what this course is about)
Concept
Circuit Model/ Analysis/Simulation

## Slide 9: Basic Electrical Engineering Design Flow
DESIGN SPECIFICATION
Ali Muhtaroğlu
CIRCUIT ANALYSIS / ENGINEERING
(what this course is about)
Concept
Circuit Model/ Analysis/Simulation
Physical
Prototype
Validation

## Slide 10: Basic Electrical Engineering Design Flow
DESIGN SPECIFICATION
Ali Muhtaroğlu
CIRCUIT ANALYSIS / ENGINEERING
(what this course is about)
Concept
Circuit Model/ Analysis/Simulation
Physical
Prototype
Validation
Validation
Physical
Design/Simulation

## Slide 11
Concept
Circuit Model/ Analysis/Simulation
Physical
Prototype
Validation
Validation
Physical
Design/Simulation
DESIGN SPECIFICATION
CIRCUIT ANALYSIS / ENGINEERING
(what this course is about)
Ali Muhtaroğlu
Basic Electrical Engineering Design Flow

## Slide 12
DESIGN SPECIFICATION
CIRCUIT ANALYSIS / ENGINEERING
(what this course is about)
Goal: Minimize the number and extend of “loops”
from a later to an earlier stage of the design flow (Cost !)
Ali Muhtaroğlu
Basic Electrical Engineering Design Flow
Concept
Circuit Model/ Analysis/Simulation
Physical
Prototype
Validation
Validation
Physical
Design/Simulation

## Slide 13
DESIGN SPECIFICATION
CIRCUIT ANALYSIS / ENGINEERING
(what this course is about)
Ali Muhtaroğlu
Basic Electrical Engineering Design Flow
Concept
Circuit Model/ Analysis/Simulation
Physical
Prototype
Validation
Validation
Physical
Design/Simulation
Main Focus of Lectures
Main Focus of Labs
Goal: Minimize the number and extend of “loops”
from a later to an earlier stage of the design flow (Cost !)

## Slide 14: Electrical Elements

## Slide 15: Basic Circuit Analysis Flow (what we will do in this class)
Problem Statement
Ali Muhtaroğlu

## Slide 16: Basic Circuit Analysis Flow (what we will do in this class)
Problem Statement
Simplified circuit diagram (visual)
Ali Muhtaroğlu

## Slide 17: Basic Circuit Analysis Flow (what we will do in this class)
Problem Statement
Simplified circuit diagram (visual)
Pick analysis method / apply creativity
Ali Muhtaroğlu

## Slide 18: Basic Circuit Analysis Flow (what we will do in this class)
Problem Statement
Simplified circuit diagram (visual)
Pick analysis method / apply creativity
Ali Muhtaroğlu
Calculate a solution

## Slide 19: Basic Circuit Analysis Flow (what we will do in this class)
Problem Statement
Simplified circuit diagram (visual)
Pick analysis method / apply creativity
Ali Muhtaroğlu
Calculate a solution
Test solution based on intuition
(or simulate)

## Slide 20: Basic Circuit Analysis Flow (what we will do in this class)
Problem Statement
Simplified circuit diagram (visual)
Pick analysis method / apply creativity
Ali Muhtaroğlu
Calculate a solution
Test solution based on intuition
(or simulate)
Understand how electrical circuits work
Learn design and analysis using lumped element models
Develop theoretical knowledge and practical lab skills useful for characterizing first and second order circuits
Get an introduction to CAD tools for design and simulation work

## Slide 21: Charge : Q or q(t) if time varying
Atoms made up of protons (with positive charge), neutrons (neutral), and electrons (with negative charge)
  A charge is bipolar i.e. either positive or negative
Unit of Charge : Coulomb (C)
Ali Muhtaroğlu

## Slide 22: Charge : Q or q(t) if time varying
Atoms made up of protons (with positive charge), neutrons (neutral), and electrons (with negative charge)
  A charge is bipolar i.e. either positive or negative
Unit of Charge : Coulomb (C)
An electron has 1.6022 x 10-19 coulomb
6.24 x 1018 electrons carry a charge of 1 coulomb
Ali Muhtaroğlu

## Slide 23: Charge : Q or q(t) if time varying
Atoms made up of protons (with positive charge), neutrons (neutral), and electrons (with negative charge)
  A charge is bipolar i.e. either positive or negative
Unit of Charge : Coulomb (C)
An electron has 1.6022 x 10-19 coulomb
6.24 x 1018 electrons carry a charge of 1 coulomb
Electric circuits are used to move charges at desired rates through circuit elements
  Motion of charge Electric fluid (current)
  Separation of charge Electric force (voltage)
Convention in this course: Positive charge moves to negative charge
Ali Muhtaroğlu

## Slide 24: Charge : Q or q(t) if time varying
Atoms made up of protons (with positive charge), neutrons (neutral), and electrons (with negative charge)
  A charge is bipolar i.e. either positive or negative
Unit of Charge : Coulomb (C)
An electron has 1.6022 x 10-19 coulomb
6.24 x 1018 electrons carry a charge of 1 coulomb
Electric circuits are used to move charges at desired rates through circuit elements
  Motion of charge Electric fluid (current)
  Separation of charge Electric force (voltage)
Convention in this course: Positive charge moves to negative charge
Ali Muhtaroğlu
Law of Conservation of Charge:
Algebraic sum of electric charges in a system is constant

## Slide 25: Atom and Charge
Electron is assumed to be negatively charged
Proton is assumed to be positively charged
Structure of atom
Neutron
Proton
Electron
Helium Atom

## Slide 26: Atom and Charge
Electron is assumed to be negatively charged
Proton is assumed to be positively charged
Structure of atom
Neutron
Proton
Electron
Helium Atom
Unit of Electrical Charge Coulomb
Definition
6.3 x 1018 electrons = 1 Coulomb
or
Electrical charge / electron = 1/ (6.3 x 1018) Coulomb
= 1.602 x 10-19 Coulomb

Atoms made up of protons (with positive charge), neutrons (neutral), and electrons (with negative charge)

## Slide 27: Current : I or i(t) if time varying
Current is time rate of change of charge:
Unit of Current: Ampere (A)
  1 A = 1 C/s
Current has a magnitude and direction
Total charge entering the element between time t1 and t2:
i
Ali Muhtaroğlu

## Slide 28: Current : I or i(t) if time varying
Current is time rate of change of charge:
Unit of Current: Ampere (A)
  1 A = 1 C/s
Current has a magnitude and direction
Total charge entering the element between time t1 and t2:
i
Ali Muhtaroğlu

## Slide 29: Current : I or i(t) if time varying
Current is time rate of change of charge:
Unit of Current: Ampere (A)
  1 A = 1 C/s
Current has a magnitude and direction
Total charge entering the element between time t1 and t2:
i
Direct
Current (DC)
Alternating
Current (AC)
Ali Muhtaroğlu

## Slide 30: Example
Determine charge entering a terminal between t=2 s and t=4 s if the current through the terminal is defined by the function:
Ali Muhtaroğlu

## Slide 31: Example
Determine charge entering a terminal between t=2 s and t=4 s if the current through the terminal is defined by the function:
Solution:
Ali Muhtaroğlu

## Slide 32: Voltage : V or v(t) if time varying
Voltage, or electromotive force (emf), or potential difference between two points a and b is the energy needed to move a unit charge from point a to b:
Unit of Voltage: Volt (V)
  1 V = 1 Joules/Coulomb = 1 Newton-meter/Coulomb
Conventions:
A
B
+
-
vo
+
-
vAB
Ali Muhtaroğlu

## Slide 33: Voltage : V or v(t) if time varying
Voltage, or electromotive force (emf), or potential difference between two points a and b is the energy needed to move a unit charge from point a to b:
Unit of Voltage: Volt (V)
  1 V = 1 Joules/Coulomb = 1 Newton-meter/Coulomb
Conventions:
A
B
+
-
vo
+
-
vAB
+
-
I
V
+
-
I
V
+
-
I
V
+
-
I
V
Energy Consumed by
the Circuit Element:
Energy Delivered by
the Circuit Element:
Ali Muhtaroğlu

## Slide 34: Passive Sign Convention
When the current through an element is in the direction of the reference voltage drop across the element, a positive sign should be used in expressions relating the voltage to the current:
  v = +f(i)
Ali Muhtaroğlu
+
-
I
V
+
-
I
V
Energy Consumed by
the Circuit Element:

## Slide 35: Passive Sign Convention
When the current through an element is in the direction of the reference voltage drop across the element, a positive sign should be used in expressions relating the voltage to the current: vice versa also true:
  v = +f(i) v = -f(i)
Ali Muhtaroğlu
+
-
I
V
+
-
I
V
Energy Consumed by
the Circuit Element:
+
-
I
V
+
-
I
V
Energy Delivered by
the Circuit Element:

## Slide 36: Standard Prefixes for Powers of 10
Ali Muhtaroğlu
Prefix | Symbol | Power | Prefix | Symbol | Power
atto | a | 10-18 | deci | d | 10-1
femto | f | 10-15 | deka | da | 10
pico | p | 10-12 | hecto | h | 102
nano | n | 10-9 | kilo | k | 103
micro | μ | 10-6 | mega | M | 106
milli | m | 10-3 | giga | G | 109
centi | c | 10-2 | tera | T | 1012

## Slide 37: Power : P or p(t) if time varying
Power is the rate at which work is being done:
Unit of Power: Joules/s (J/s) or Watts (W)
Ali Muhtaroğlu

## Slide 38: Power : P or p(t) if time varying
Power is the rate at which work is being done:
Unit of Power: Joules/s (J/s) or Watts (W)
Ali Muhtaroğlu

## Slide 39: Power : P or p(t) if time varying
Power is the rate at which work is being done:
Unit of Power: Joules/s (J/s) or Watts (W)
Energy delivered to an element between time t1 and t2:
Ali Muhtaroğlu

## Slide 40: Power : P or p(t) if time varying
Power is the rate at which work is being done:
Unit of Power: Joules/s (J/s) or Watts (W)
Energy delivered to an element between time t1 and t2:
Ali Muhtaroğlu

## Slide 41: Power : P or p(t) if time varying
Power is the rate at which work is being done:
Unit of Power: Joules/s (J/s) or Watts (W)
Energy delivered to an element between time t1 and t2:
Conventions:
+
-
I
V
+
-
I
V
+
-
I
V
+
-
I
V
The element is
consuming power (+)
The element is
delivering power (-)
In a circuit:
Ali Muhtaroğlu

## Slide 42: Example
A stove draws 10 A when connected to a 120-V line. How long does it take to consume 30kJ ?
Ali Muhtaroğlu

## Slide 43: Example
A stove draws 10 A when connected to a 120-V line. How long does it take to consume 30kJ ?
Solution:
Ali Muhtaroğlu

## Slide 44: Example 2
A notebook computer has a total power consumption of 50 W when running an ‘average’ application. The battery used in this notebook has a capacity of 300 Whrs (Watt-hours). What is the average battery life of this notebook?
Ali Muhtaroğlu

## Slide 45: Example 2
A notebook computer has a total power consumption of 50 W when running an ‘average’ application. The battery used in this notebook has a capacity of 300 Whrs (Watt-hours). What is the average battery life of this notebook?
Solution:
Ali Muhtaroğlu
Note how Watt-hours is sometimes used as the unit of energy
instead of Joules.

## Slide 46: Passive & Active Elements
The energy absorbed by a Passive element up to any time t must be nonnegative:
Ali Muhtaroğlu

## Slide 47: Passive & Active Elements
The energy absorbed by a Passive element up to any time t must be nonnegative:
The opposite is true for Active elements.
Some active elements:
Independent Voltage Source:
Independent Current Source:
Voltage is fixed, independent of current
Current is fixed, independent of voltage
Ali Muhtaroğlu