## Slide 1
Dr. Özçel Cangül
Lecture Notes by Dr. Ali Muhtaroğlu
Fall 2023
METU Northern Cyprus Campus
References:
Electric Circuits 10th Ed. by Nilsson & Riedel
Electrical Circuit Analysis 3rd Ed. by Johnson, Johnson, Hilburn, and Scott
Engineering Circuit Analysis 7th Ed. by Hayt, Kemmerly, and Durbin
Fundamentals of Electric Circuits 3rd Ed. by Alexander, and Sadiku
Electrical Circuits EEE-281 Lecture Notes

## Slide 2: Circuit Elements, Ohm’s and Kirchhoff’s Laws Weeks 2-3 Reading: Nilsson & Riedel Chapter 2
Ali Muhtaroğlu

## Slide 3: Lumped-Parameter Circuit Model
An electrical circuit is fully characterized by:
Elements it contains
How the elements are interconnected
+
-
Ali Muhtaroğlu

## Slide 4
An electrical circuit is fully characterized by:
Elements it contains
How the elements are interconnected
Wires are perfect conductors;
cannot accummulate charge,
cannot dissipate energy
+
-
Ali Muhtaroğlu
Lumped-Parameter Circuit Model

## Slide 5: Lumped-Parameter Circuit Model
An electrical circuit is fully characterized by:
Elements it contains
How the elements are interconnected
Wires are perfect conductors;
cannot accummulate charge,
cannot dissipate energy
Energy lumped within elements
+
-
Ali Muhtaroğlu

## Slide 6: Lumped-Parameter Circuit Model
An electrical circuit is fully characterized by:
Elements it contains
How the elements are interconnected
Wires are perfect conductors;
cannot accummulate charge,
cannot dissipate energy
Energy lumped within elements
+
-
Node: A point where two or more circuit elements meet
Ali Muhtaroğlu

## Slide 7
The terminal voltage of an ideal voltage source is constant, regardless of the current flowing in those terminals. The voltage source is independent if it establishes a voltage across its terminals without relying on voltages or currents elsewhere in the circuit.
The current of an ideal current source is constant, regardless of the voltage across its terminals. The current source is independent if it establishes a current without relying on voltages or currents elsewhere in the circuit.
Ali Muhtaroğlu
Ideal Independent Sources
OR

## Slide 8
The terminal voltage of a dependent (controlled) voltage source depends on a voltage or a current defined at some other location in the circuit. Two types are:
VCVS : Voltage-controlled voltage source
CCVS : Current-controlled voltage source
The current of a dependent (controlled) current source depends on a voltage or a current defined at some other location in the circuit. Two types are:
VCCS : Voltage-controlled current source
CCCS : Current-controlled current source
Ali Muhtaroğlu
Dependent Sources

## Slide 9
VCVS: CCVS:
VCCS: CCCS:
Ali Muhtaroğlu
Dependent Sources (Linear Controlled)
μ : voltage gain (dimensionless)
β : current gain (dimensionless)
r : transresistance (ohms)
g : transconductance (siemens)

## Slide 10: Series Voltage Sources
Ali Muhtaroğlu
A chain of series voltage sources is equivalent to a single voltage source whose source function is the algebraic sum of the series source functions.
≡

## Slide 11: Series Voltage Sources
Ali Muhtaroğlu
A chain of series voltage sources is equivalent to a single voltage source whose source function is the algebraic sum of the series source functions.
≡
≡
The series current source functions have to be all equal in a chain of series current sources, in which case the chain is equivalent to any one of them. Otherwise there is a mathematical inconsistency.
Series Current Sources

## Slide 12: Parallel Current Sources
Ali Muhtaroğlu
A set of parallel current sources is equivalent to a single current source whose source function is the sum of the parallel source functions.
≡

## Slide 13: Parallel Current Sources
Ali Muhtaroğlu
A set of parallel current sources is equivalent to a single current source whose source function is the sum of the parallel source functions.
≡
≡
A set of voltage sources in parallel must have equal source functions in which case any one of them is equivalent to the entire set. Otherwise there is a mathematical inconsistency.
Parallel Voltage Sources

## Slide 14: Example
For the circuit shown, a) what value of vg is required in order for the interconnection to be valid? b) For this value of vg, find the power associated with the 8 A source.
Ali Muhtaroğlu

## Slide 15: Example
For the circuit shown, a) what value of vg is required in order for the interconnection to be valid? b) For this value of vg, find the power associated with the 8 A source.
ib = -8 A and vg = ib /4 = -2 V
b) P = V . I = -2 V . 8 A = -16 W (16 W delivered or generated)
Ali Muhtaroğlu
Solution

## Slide 16: Example 2
If the interconnection in the below figure is valid, find the power developed by the current sources. If the interconnection is not valid, explain why.
Ali Muhtaroğlu

## Slide 17: Example 2
If the interconnection in the below figure is valid, find the power developed by the current sources. If the interconnection in not valid, explain why.
There are no inconsistencies (different voltage sources connected in parallel, or different current sources connected in series).
The total power of the current sources is:
10A.100V + 5A.140V=1700 W
Ali Muhtaroğlu
Solution

## Slide 18: Example 3
If the interconnection in the below figure is valid, find the total power developed by the voltage sources. If the interconnec-tion is not valid, explain why.
Ali Muhtaroğlu

## Slide 19: Example 3
If the interconnection in the below figure is valid, find the total power developed by the voltage sources. If the interconnec-tion in not valid, explain why.
The 4 A and 5 A current sources connected in series create an inconsistency. This interconnection is not valid.
Ali Muhtaroğlu
Solution

## Slide 20: Resistance and Resistivity
For a given conductor with length l, and cross-sectional area A:
where ρ is the material resistivity.
Ali Muhtaroğlu
A
l

## Slide 21: Ohm’s Law
The voltage across a resistor is directly proportional to the current flowing through the resistor.
Power consumed by a resistor:
R : Resistance in Ohm (Ω)
R ≥ 0
Ali Muhtaroğlu

## Slide 22: Conductance (G)
Unit: Siemens (S) or Mho ( )
Ali Muhtaroğlu
Ω

## Slide 23: Example
i) Calculate the value of v and i in the following circuits. ii) Determine the power dissipated in each resistor.
Ali Muhtaroğlu

## Slide 24: Example
i) Calculate the value of v and i in the following circuits. ii) Determine the power dissipated in each resistor.
Ali Muhtaroğlu
Solution
i) va = (1)(8)=8 V ; ib = (50)(0.2)=10 A ; vc = -(1)(20)=-20 V ; id = -50/25= -2 A
ii)

## Slide 25
A short circuit is a perfect conductor or conductor with zero resistance. Two nodes can be short circuited by connecting them with a wire. A short circuit can sustain current without any voltage drop. [In reality, there always is a max. current limit after which damage occurs to the material.]
An open circuit is a perfect insulator or resistor with zero conductance. An open circuit can sustain any voltage without any flow of current. [Again there is always a max. practical limit after which breakdown occurs.]
(Circuit modeling: Read Nilsson Examples 2.4, 2.5)
Ali Muhtaroğlu
Short Circuit
Open Circuit

## Slide 26: Kirchhoff’s Current Law (KCL)
The sum of the currents entering any node equals the sum of the currents leaving the node.
(The algebraic sum of all the currents at any node in a circuit equals zero.)
+
-
i3
i4
Ali Muhtaroğlu
i2
i1
i5

## Slide 27: Kirchhoff’s Current Law (KCL)
The sum of the currents entering any node equals the sum of the currents leaving the node.
(The algebraic sum of all the currents at any node in a circuit equals zero.)
i2 + (– i1) = 0
Our convention:
+ for currents exiting the node
- for currents entering the node
Ali Muhtaroğlu
+
-
i3
i4
i2
i1
i5
i3 + i4 + (– i2) = 0
i5 + (– i3) = 0

## Slide 28: Kirchhoff’s Voltage Law (KVL)
The sum of voltage drops around any closed path is zero.
+
-
v1
+
-
v2
+
-
v3
+
-
v4
+
-
Ali Muhtaroğlu

## Slide 29: Kirchhoff’s Voltage Law (KVL)
The sum of voltage drops around any closed path is zero.
+
-
v1
+
-
v2
+
-
v3
+
-
v4
+
-
Our convention:
+ if traversing + to – terminal clockwise
- if traversing – to + terminal clockwise
(-v1) + v2 + v3 = 0
Ali Muhtaroğlu

## Slide 30: Kirchhoff’s Voltage Law (KVL)
The sum of voltage drops around any closed path is zero.
+
-
v1
+
-
v2
+
-
v3
+
-
v4
+
-
(-v3) + v4 = 0
Our convention:
+ if traversing + to – terminal clockwise
- if traversing – to + terminal clockwise
(-v1) + v2 + v3 = 0
Ali Muhtaroğlu

## Slide 31: Example
An electric circuit was built as below. Use KCL and KVL to solve for unknown current and voltages:
v1
-
+
1 V
-
+
1 V
+
-
i2
i1
i4
i3
2A
+
-
4 V
v3
-
+
v2
-
+
v4
-
+
Ali Muhtaroğlu

## Slide 32: Example
An electric circuit was built as below. Use KCL and KVL to solve for unknown current and voltages:
Due to lumped-parameter assumptions, wires are perfect conductors. Therefore, v2= v4 = 0. v3 =- v1 . i1= i3=0, because there is no closed circuit loop for current to flow. i2= i4=2 A using KCL, and v1 =-2V using KVL.
Ali Muhtaroğlu
v1
-
+
1 V
-
+
1 V
+
-
i2
i1
i4
i3
2A
+
-
4 V
v3
-
+
v2
-
+
v4
-
+

## Slide 33: Example 2
Use KCL and KVL to solve for unknown current and voltages:
v1
-
+
v2
+
-
5 V
+
-
3 V
+
-
11 V
-
+
9 V
-
+
2 V
-
+
i4
1 A
2 A
6 A
i8
i7
i6
10 A
i5
i3
-3 A
Hint: 8 unknowns require 8 independent equations to solve
Ali Muhtaroğlu

## Slide 34: Example 2 (continued)
8 unknowns : Require 8 independent equations to solve
KVL:
KCL:
Solving all:
Ali Muhtaroğlu

## Slide 35: Example 3 (Ex 2.10)
Use Kirchhoff’s laws and Ohm’s law to find the voltage v0 as shown below.
Show that your solution is consistent with the constraint that the total power developed in the circuit equals the total power dissipated.
Ali Muhtaroğlu

## Slide 36: Example 3 (Ex 2.10)
Use Kirchhoff’s laws and Ohm’s law to find the voltage v0 as shown below.
Show that your solution is consistent with the constraint that the total power developed in the circuit equals the total power dissipated.
Ali Muhtaroğlu
Solution:

## Slide 37: Example 4 (AP 2.10)
The current iΦ in the circuit shown is 2 A. Calculate:
a) vs ; b) The power absorbed by the independent voltage source,
c) The power delivered by the independent current source,
d) The power delivered by the controlled current source,
e) The total power dissipated in the two resistors.
Ali Muhtaroğlu

## Slide 38: Example 4 (AP 2.10)
The current iΦ in the circuit shown is 2 A. Calculate:
a) vs ; b) The power absorbed by the independent voltage source,
c) The power delivered by the independent current source,
d) The power delivered by the controlled current source,
e) The total power dissipated in the two resistors.
Ali Muhtaroğlu
Solution:
i1

## Slide 39: Example 4 (AP 2.10)
The current iΦ in the circuit shown is 2 A. Calculate:
a) vs ; b) The power absorbed by the independent voltage source,
c) The power delivered by the independent current source,
d) The power delivered by the controlled current source,
e) The total power dissipated in the two resistors.
Ali Muhtaroğlu
Solution (continued):
i1
is
+
-
v1
+
-
vϕ